Notes concerning the use of the 100 page PDF file for testing in accordance with ISO/IEC 19752.

Creation of this test suite was at the request of several SC28 members who do not have the ability to number pages while printing.  As stated in ISO/IEC 19752:2004 clause 4.7 a header or footer can be added to the test file.  The provided file, when sent to the printer using a PDF reader and appropriate printer driver will produce a job containing 100 pages of the ISO/IEC 19752 test page with numbers in the upper left hand corner.  Care should be taken when using this 100 page file.

- If there is a jam during printing, the page count provided by the PDF file will be wrong

- When a fade occurs, the printer will continue to print.  Any pages printed after fade cannot be included in the yield calculation.  If the printer is stopped after fade, the page count will be wrong.

- The page number printed at the top of the page may not be the actual page printed due to jams, mis-feeds or driver issues.

It is the responsibility of the individual using the modified test page to assure that the page count and yield results obtained using the modified test page would be equivalent to the results using the single page test file.